| FREQUECY INDEPENDENT DATA |
| --- |
| Description: | cross-polarized stacked yagi array, dual feed, physically quarter wavelength along the boom phased |
| Frequency: | 380-410 MHz, 405-440 MHz, 440-475 MHz, 830-890 MHz, 890-960 MHz |
| Impedance: | 50 ohm |
| Gain: | 9 dBi |
| Polarization: | dual/circular |
| Isolation: | 30 dB |
| Connector: | 2*N-female/2*TNC-female |
| VSWR: | < 1.5 |
| Radome: | UV resistant fiberglass/ABS, RAL 7012, PU foam filling |
| Radiator: | copper |
| Passive elements: | coated aluminium |
| Attachment: | Ø 35-60 mm, aluminium alloy bracket, stainless steel V-bolts and self-locking nuts |
| Lightning protection: | DC-short circuited |
| Temperature: | -35° - +80° C |
| IP: | 67 |

# Text boxes

ComAnt® Communications Antennas

## CAXS2 CROSS-POLARIZED STACKED YAGI ARRAY

L